## Slide 1: Comparison of PDE-based, Gaussian and Wavelet Approaches for Enhancing PET Images
By:
Abeer Mohtaseb
Najla Bazaya
Oraib Horini
Supervised by:
Dr.Musa Alrefaya

## Slide 2: Contents:
  Introduction
  Study Objectives
  Study Importance
  Methodology
  Study Schedule
  Image De-noising

## Slide 3: Introduction
The PET image which use to diagnose the cancer disease suffer from noise, this leads to misdiagnosis.

## Slide 4: Study Objectives
This research aims to make a comparison between filters which may use in de-noising for PET image to study the effects of the filters to enhance the PET medical image in order to achieve ideal image to detect diseases.

## Slide 5: Study Importance
Helping physicians for better diagnosing patients using PET image .
Decrease the false positive and false negative results.

## Slide 6: Methodology
Demonstrate qualitative and through simulations.
The validation of the proposed filter employs simulated PET data of a slice of the thorax.
The used methods for comparing the filters results are: PSNR, NR, and correlation.

## Slide 7: Image De-noising
Noise: is undesired information that contaminates the image.
De-noising: is the first step to be taken before the images data is analyzed.

## Slide 8: Image filtering
Gaussian Filter .
Wavelet transform .
Anisotropic Diffusion Filter .
Mean Curvature Motion .

## Slide 9: Gaussian Filter
Done by convoluting each point in the input array with gaussian kernel then summing all to produce the output array.
Gaussian for 2D:
σ : standard deviation.
High σ leads to a higher degree of smoothness.

## Slide 10: Wavelet transform
Represents a signal as a sum of translations and dilations of a band-pass function.
A signal can be decomposed using multi resolution analysis:

## Slide 11: Anisotropic Diffusion Filter
Perona and Malik Equation:
I (t) = div(c (t, x, y) delta I)
c (t, x, y) is the edge stopping.
x is the gradient magnitude.
But when c(t, x, y) = 1..Whats happened??

## Slide 12: Cont..
Perona has improved it and give an image function g(x):
g(x) = 1/1+(x/k)(x/k)
Or
g(x) = exp((x/k)(x/k))
K:control the sensitivity to edges.

## Slide 13: Mean Curvature Motion
By curve (u)(x), we denote the curvature, i.e. the signed inverse of the radius of curvature of the level line passing by x. When Du(x) 6= 0, this means :
curve(u)=

## Slide 14: Quantitative Evaluation Measure
1. Peak Signal-to-Noise Ratio (PSNR):
Is the ratio of a signal power to the noise power.

## Slide 15: Cont..
2. Noise Variance (NV):
describes the remaining noise level .So, it should be a small as possible.
How will we estimate the noise variance?
Noise variance = Variance of the image

## Slide 16: Cont..
3. Correlation:
Correlation between the image and the correlation filter, the better quality when this correlation is high.
Where F: is a Correlation Filter.
I: image.
And i, j are denote to the position in image and in correlation filter.

## Slide 17: Implementation & results

## Slide 18: De-noising quality measure (FBP PET image reconstruction)
 | Noise fbp | Perona & Malik | Gaussian | Wavelet | Curvature
PSNR | 12.1155 | 21.9530 | 16.9102 | 18.6044 | 22.9178
Correleion | 0.6922 | 0.9681 | 0.9323 | 0.9591 | 0.9673
NV | 0.0696 | 0.0236 | 0.0971 | 0.0850 | 0.0238

## Slide 19: FBP PET image reconstruction
Noise image Original image
Perona Gaussian Curvature Wavelet

## Slide 20: De-noising quality measure (OSEM PET image reconstruction)
 | Noise osem | Perona& Malik | Gaussian | Wavelet | Curvature
PSNR | 22.9196 | 32.5611 | 21.5641 | 21.7255 | 27.4822
Correlation | 0.7948 | 0.9805 | 0.9777 | 0.9786 | 0.9701
NV | 0.0652 | 0.0216 | 0.0758 | 0.0743 | 0.0367

## Slide 21: OSEM PET image reconstruction
Noise image Original image
Perona Gaussian Curvature Wavelet

## Slide 22: Conclusion
PDE-based filters (Perona & Malik and CCM) are the best.

## Slide 23: Recommendation
Our team recommended increasing the number of filters in the comparison process to get the better de-noising result of the PET as possible.

## Slide 24: References
[1] Goldberg, A, Zwicker, M, Durand, F. Anisotropic Noise. University of California, San Diego MIT CSAIL.
[2] Shidahara, M, Ikomo, Y, Kershaw, J, Kimura, Y, Naganawa, M, Watabe, H. PET kinetic analysis: wavelet denoising of dynamic PET data with application to parametric imaging. Ann Nucl Med. 21. 379–386. (2007).
[3] Greenberg, Sh and Kogan, D. Anisotropic Filtering Techniques applied to Fingerprints. Vision Systems - Segmentation and Pattern Recognition. 26. 495-499. (2007).
[4] Gerig, G, Kubler, O, Kikinis, R and Jolesz, F. A. Nonlinear Anisotropic Filtering of MRI Data. IEEE TRANSACTIONS ON MEDICAL IMAGING. 1(2). 221-224. (1992).
[5] Olano, M, Mukherjee, Sh and Dorbie, A. Vertex-based Anisotropic Texturing.

## Slide 25: Summary

## Slide 26
Thank You